## Slide 1
Work order issue flow — both options
Outbound
Same trigger and same destination. The difference is how the work order travels in between.
Option 1 — API hub: direct, sequential issue
L3 Persist
Dataverse change
entity updated
L2 Orch
WO Issuer FA
build work order
L2 Orch
Vendor resolver
channel + format
L4 Deliver
Adapter
format + push
external
Vendor
receives WO
One call after another — simple to follow. A slow vendor holds the chain; no built-in replay.
Option 2 — event-driven: event-triggered, parallel-capable issue
Event
RepairAssigned
event raised
L2 Orch
WO Issuer FA
build work order
L2 Orch
Vendor resolver
channel + format
L2 Orch
Durable fan-out
retry per branch
L4 Deliver
Adapter → vendor
deliver to one vendor
Triggered by an event, delivered with per-branch retry, and replayable — one vendor down never blocks others.
Shared by both: one work order always goes to one vendor. The issuer and resolver are identical; only the delivery mechanism differs — a direct call (Option 1) versus an event-triggered, retry-per-branch fan-out (Option 2).

## Slide 2
Architecture principles
The rules that hold across both options — they are what make the platform scale to 50+ vendors.
Operation-centric, not vendor-centric
The platform is built around what happens — create a repair, issue a work order, update status — not around who the vendor is. Vendors are configuration behind a shared operation, never bespoke pipelines.
Contract first
Here is our form — fill it in our way.
We publish one fixed request format. Every vendor matches it, so we stop writing a custom translator for each one.
Shared core, thin edges
One engine in the middle, a small plug per vendor.
The real work is built once and reused. Only a tiny vendor-specific piece (their format and address) sits at the edge.
One operation, one path
All roads merge once you are through the door.
However a vendor arrives — web, file, email — the request follows the same internal route. One path to secure and watch.
Config over code
Adding a vendor is a form, not a project.
Onboarding is filling in settings and credentials, not building and deploying new software. The 51st vendor is easy.
One source of truth
Shortcuts never pretend to be the real answer.
Dataverse holds the official record. Fast cached copies speed reads but are never treated as authoritative.
See everything in one place
One window, not fifty places to check.
Because every operation crosses one front door, logs, metrics, and failures show up in a single dashboard for all vendors.

## Slide 3
Observability and resilience
How we see what is happening, and how the platform keeps working when something fails.
Observability stack
APIM analytics
Who called what, how often, success vs error — seen right at the front door.
Application Insights
Traces one request end to end across the receiver, handler, and adapters.
Log Analytics
One place to search every log with queries, across all vendors at once.
Azure Monitor + alerts
Dashboards and automatic alerts — queue backing up, error spike, dead-letters.
Resilience patterns
Buffer + 202 — accept, queue, reply at once — a downstream slow-down never blocks the vendor.
Retry with backoff — a failed write retries automatically, waiting longer each time before giving up.
Dead-letter queue — anything that keeps failing is parked safely for review, never silently lost.
Idempotency keys — the same message arriving twice is processed once — no duplicate work orders.
Per-branch isolation — each vendor delivery retries on its own; one vendor down never stalls others.
Event replay (Option 2) — re-run missed work orders for an offline vendor from any point in time.